Cougar v1.10 firmware configurable parameters

Parameter	Abbreviation	Range	Default	Description

Kp	kp	0 - 500	2	Proportional gain for motor current	controlling PI loop.

Ki	ki	0 - 500	160	Integral gain for motor current	controlling PI loop.

throttle_min_raw_counts	t-min-rc	0 - 1023	413	Raw ADC counts for floored throttle.

throttle_max_raw_counts	t-max-rc	0 - 1023	683	Raw ADC counts for released	throttle.

throttle_fault_raw_counts	t-fault-rc	0 - 1023	100	Raw ADC counts for throttle fault –	if ADC counts for throttle is <=	throttle_fault_raw_counts for 200mS	throttle fault is latched.

throttle_pos_gain	t-pos-gain	0 - 128	8	CR (current reference) = TR (throttle)	[0 to 511] * throttle_pos_gain / 8 -	PWM [0 to 511] * throttle_pwm_gain	/ 8

throttle_pwm_gain	t-pwm-gain	0 - 128	0	If throttle_pwm_gain = 0 CR (current	reference) is proportional to TR	(throttle). If throttle_pwm_gain > 0	CR decreases as PWM (motor	voltage) increases, approximating	Curtis 1231C behavior.

current_ramp_rate	c-rr	0 - 100	6	Current ramp rate in amps per	millisecond. Zero disables CR	(current reference) change.

rtd_period	rtd-period	0 - 32000	0	Period for real time data updates (in	milliseconds). Zero disables real	time data updates.

pwm_filter	pwm-filter	0 - 3	0	Sets the speed of the low pass filter	used for PWM used by	throttle_pwm_gain. 0 is slowest and 3	is fastest.

motor_os_threshold	motor-os-th	0 - 9999	0	Threshold for motor overspeed	detection. Larger number means	higher speed.

motor_os_ftime	motor-os-ft	0 - 9999	1000	Motor overspeed fault is	automatically cleared in the specified	number of milliseconds.

motor_os_dtime	motor-os-dt	0 - 99	10	Motor overspeed detection time in	milliseconds. Motor must be in	overspeed state for specified time	before motor overspeed fault is set.

pwm_deadzone	pwm-deadzone 0 - 99	5	Specifies at how many PWM counts	the MOSFETs begin to conduct.

motor_speed_calc_amps	motor-sc-amps 0 - 511	0	Motor current (CF) must be >	motor_speed_calc_amps to calculate	motor speed. Helps eliminate false	motor overspeed tripping when gas
pedal is released.

battery_amps_limit	bat-amps-lim 0 - 511	0	Battery current limit in amps. Zero	disables battery amps limiting.

precharge_time	pc-time	0 - 999	0	Capacitor bank precharge time in	tenths of seconds. Zero disables	precharg timer.

Cougar v1.10 firmware commands

config	Shows all configurable parameters.

save	Saves all configurable parameters from volatile memory to EE Prom.

idle	Shows micro-controller idle time percentage.

restart	Restarts (resets) the micro-controller.

reset-ah	Resets the calculated battery amp hours meter.